## Slide 1: ENGI 301 Dispenser PCB Proposal
11/19/2018
Nicholas Lester

## Slide 2: Board Functionality
I am proposing to make a PCB for my Skittle dispenser with the following functions:
  Plugs into the pins on the PocketBeagle
  Gets its power from a barrel connector
  Has two piezo elements attached to the board
  Has one i2c hex display on the board
  Has 100 mil male headers for the servo connectors
  Has 100 mil female headers for the IR breakbeam and force sensitive resistor connectors

## Slide 3: System Block Diagram
PCB
Barrel Connector
Barrel Input
PWM1
Micro Servo
AIN5
FSR
I2C1_SCL
I2C1_SDA
Adafruit 4-Digit Display
GPIO59
IR Sensor
Piezo Element
PWM2
Piezo Element
PWM0_A

## Slide 4: Power Block Diagram
PCB
Barrel Connector
Barrel Input
SYS_VOUT
Micro Servo
3.3V_OUT
FSR
SYS_3.3V
Adafruit 4-Digit Display
3.3 Volts
~ 160 mA
3.3 Volts
5 Volts
~ 1 mA
3.3 Volts
3.5 mA
Piezo Element
IR Sensor Part 2
IR Sensor Part 1
SYS_3.3V
5 Volts
20 mA total
SYS_3.3V
3.3 Volts
~ 3 mA
3.5 mA
Piezo Element
SYS_3.3V
3.3 Volts

## Slide 5: Layout Block Diagram
Hex Display
2” x 0.75”
2”
3”
Piezo Element
1.125” Diameter
Piezo Element
1.125” Diameter
Front
PocketBeagle Connections Area
2” x 1.25”
3”
2”
FSR Connection Pad Area
IR Connections Area
IR Connections Area
Servo Connections Area
Barrel Connector
Back